## Slide 1
FORCING SUB-PROJECT
Informed forcing for CONUS-wide NWM
A user guide to the data—not just the files
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
01
1 km
NWM target grid
1 hour
Time resolution
2 streams
NRT + Retro
Best available evidence • Physically consistent fields • Traceable revisions
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.

## Slide 2
PRODUCT GUIDE
Better informed—not simply higher resolution
Four design goals shape every production choice.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
02
Use observations
Prefer credible measurements; retain model
coverage.
Respect terrain
Adjust meteorology to NWM elevation.
Keep consistency
Temperature, pressure, humidity and
longwave stay coupled.
Explain changes
Record sources, quality checks and
revisions.
A finer grid is not proof of greater accuracy.
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.
NLDAS forcing: https://ldas.gsfc.nasa.gov/nldas/v2/forcing

## Slide 3
PRODUCT GUIDE
Eight fields, one model-ready product
Hourly meteorology on the NWM grid; daily files for efficient access.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
03
RAINRATE
Precipitation
kg m⁻² s⁻¹
T2D
2-m temperature
K
Q2D
2-m specific
humidity
kg kg⁻¹
PSFC
Surface pressure
Pa
SWDOWN
Downward
shortwave
W m⁻²
LWDOWN
Downward
longwave
W m⁻²
U2D
10-m eastward wind
m s⁻¹
V2D
10-m northward
wind
m s⁻¹
Daily file = 24 hourly records. It does not mean daily-resolution data.
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.

## Slide 4
PRODUCT GUIDE
One production chain, two published streams
Native source grids map directly to NWM—no common 4-km intermediate grid.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
04
Acquire
Sources +
revisions
Build baseline
Select • remap •
adjust
Constrain
PRISM +
consistency
Publish
Audit •
provenance
Terrain • masks • cached weights
NRT
Retro
Baseline is shared working data; NRT and Retro remain separate products.
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.

## Slide 5
PRODUCT GUIDE
Observation-informed inputs
Nominal source grids and update timing—not delivery guarantees.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
05
Source
Native grid / time
Availability / revisions
Main contribution
MRMS
~1 km / hourly QPE
Pass 1 ~20 min
Pass 2 ~60 min*
Storm timing +
radar/gauge detail
Stage-IV
~4 km / 1 h + 6 h
Hours; RFC-dependent
Later revisions
Regional radar/gauge QC
PRISM
4 km / daily
First ~1 day
Stable ~6 months
Rain totals + Tmin/Tmax
*Current MRMS latency. Older versions: ~1 / 2 hours. Actual availability varies.
Notes: MRMS current operational tables indicate approximately 20-minute Pass 1 and 60-minute Pass 2 latency. Older versions used approximately 60 and 120 minutes. Stage-IV availability and revisions vary by RFC and accumulation period; no universal latency is asserted. PRISM uses the 4-km archive in this project, although other resolutions exist.
Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.
MRMS: https://www.nssl.noaa.gov/projects/mrms/operational/tables.php
MRMS versions: https://inside.nssl.noaa.gov/mrms/past-code-updates/
Stage IV: https://www.emc.ncep.noaa.gov/mmb/research/stage4.FAQ.html
PRISM: https://www.prism.oregonstate.edu/calendar/
PRISM grids: https://prism.oregonstate.edu/data/

## Slide 6
PRODUCT GUIDE
Complete meteorology across time and space
Complementary roles—not a “reanalysis always wins” rule.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
06
Source
Native grid / time
Availability / cycles
Role in this product
NLDAS-2
0.125° / hourly
~4-day lag
Consistent historical
backbone
HRRR
3 km / hourly
Hourly cycles
Publication lag varies
Recent hourly analysis;
forecast rain
GFS
0.25° / hourly leads
00 / 06 / 12 / 18 UTC
Leads 1–6; backup ≤12
Required northern NRT
coverage
GFS is a short-forecast gap filler—not an hourly analysis or Retro source.
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.
NLDAS: https://ldas.gsfc.nasa.gov/nldas
NLDAS forcing: https://ldas.gsfc.nasa.gov/nldas/v2/forcing
HRRR: https://emc.ncep.noaa.gov/emc/pages/numerical_forecast_systems/hrrr.php
GFS: https://www.nco.ncep.noaa.gov/pmb/products/gfs/

## Slide 7
PRODUCT GUIDE
The same date becomes better informed
Illustrative data age—not a guaranteed product-delivery timeline.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
07
Hours
MRMS / Stage-IV
HRRR + GFS
~1 day
Early PRISM
constraints
~4 days
NLDAS-2
replaces
HRRR / GFS
~6 months
Stable PRISM
Retro eligibility
NRT: mutable as observations and revisions arrive
Retro: stable
Check actual completeness and revisions—not age alone.
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.
PRISM: https://www.prism.oregonstate.edu/calendar/
NLDAS: https://ldas.gsfc.nasa.gov/nldas
MRMS: https://www.nssl.noaa.gov/projects/mrms/operational/tables.php

## Slide 8
PRODUCT GUIDE
Precipitation: select locally, constrain daily
Quality and coverage can change the preferred source from cell to cell.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
08
Eligible sources
MRMS passes
Stage-IV
NLDAS-2 → HRRR
Hourly composite
Quality + coverage
Regional exceptions
Preserve valid zeros
PRISM constraint
Adjust daily amount
Retain hourly timing
Guard dry/wet cases
GFS fills unsupported northern rain only; it never overwrites valid rain.
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.

## Slide 9
PRODUCT GUIDE
PRISM changes the amount—not the storm clock
Schematic example: hourly pattern × 1.5 gives the PRISM daily total.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
09
Hourly composite: 12 mm
Time within PRISM day →
PRISM-constrained: 18 mm
Time within PRISM day →
PRISM 12–12 windows are internal. Published files remain 00–23 UTC.
Notes: Illustration only, not observed data. Production uses PRISM 12–12 UTC accumulation windows, then regroups output into calendar-day files. Real reconciliation includes validity, dry/wet, scaling and domain checks, so not every cell follows an unconstrained ratio.
Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.
PRISM: https://www.prism.oregonstate.edu/calendar/

## Slide 10
PRODUCT GUIDE
Terrain corrections stay physically coupled
Elevation-aware downscaling follows the Cosgrove framework.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
10
Temperature
Fixed lapse-rate
elevation
adjustment
Pressure
Hydrostatic
profile
using
temperature
Humidity
Interpolate RH
Recompute
specific humidity
Longwave
Adjust effective
emission
temperature
PRISM temperature revisions also update humidity and longwave.
Rotate wind vectors correctly. Preserve nighttime shortwave behavior.
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.
Cosgrove: https://doi.org/10.1029/2002JD003118

## Slide 11
PRODUCT GUIDE
The northern HRRR gap must not stop NWM
GFS completion is required for HRRR-selected NRT hours.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
11
GFS: northern coverage
HRRR: native coverage
Conceptual footprint—not a geographic map
NLDAS-2 available?
Use NLDAS-2; no GFS needed.
Otherwise: HRRR + GFS
Missing required GFS → preserve old file.
Keep active NWM cells covered; avoid unnecessary offshore extrapolation.
Notes: Diagram is conceptual, not a geographic map. Actual coverage uses cached native-HRRR geometry and the versioned static envelope. Do not infer a latitude boundary from the rectangles. NLDAS-2 selection is per hour. GFS uses one meteorological bundle/cycle and elevation adjustments; valid precipitation is preserved. Missing required GFS fails the affected update, retaining previously accepted files.
Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.
GFS: https://www.nco.ncep.noaa.gov/pmb/products/gfs/

## Slide 12
PRODUCT GUIDE
NRT and Retro answer different questions
Keep both: timeliness can be evaluated against the later stable product.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
12
NRT
What could operations know?
Recent, revisable sources
Early PRISM when eligible
NLDAS replacement as it arrives
Retro
What is our stable reconstruction?
NLDAS-2 backbone
Best eligible precipitation
Stable PRISM constraints
Retro does not overwrite NRT. Record the version used in each simulation.
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.

## Slide 13
PRODUCT GUIDE
NRT: refresh → replace only what changed
Dependency fingerprints let unchanged baselines and windows be reused.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
13
Refresh inputs
Check completeness
and source revisions
Resolve changes
NLDAS arrival?
PRISM revision?
Rebuild + audit
Reuse valid work
Replace atomically
Required GFS acquisition is part of the recent-hour production path.
A failed update must not replace accepted data with incomplete output.
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.

## Slide 14
PRODUCT GUIDE
Scheduled opportunities ≠ current-hour delivery
Repository schedule template • not yet installed on the inspected host
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
14
Lane
UTC schedule
Current scan / behavior
NRT
02 / 14 / 20
10 target days; skip unchanged
Daily NRT
08 each day
200-day deeper revision check
Retro
10 on the 18th
45-day eligibility window; stable only
NRT endpoint: UTC today − 2 days. No partial-current-day delivery.
Status report template: every 2 hours • 7-day recent GFS-aware processing tail
Notes: Source: cron/hydro_ops.crontab and bin/update_nwm_forcing.py cycle_window, checked 2026-09-19. Six-hourly target scan 10 days with 14-day source repair lookback; daily 200 days; recent GFS worker tail seven days. Both NRT lanes end at UTC today minus two days. Monthly retro scans 45 target days ending today minus 183 days and still requires stable PRISM acceptance. These are scan windows, not mandatory rebuild counts. Faster event-driven/current-day delivery and daily retro eligibility scans are proposed, not activated.
Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.

## Slide 15
PRODUCT GUIDE
Retro: stable constraints, reproducible history
Source availability changes across eras; the common product contract does not.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
15
1979–1980
NLDAS-2
Monthly PRISM
1981–2001
NLDAS-2
Daily PRISM
2002 onward
Add Stage-IV
Daily PRISM
Modern era
Add MRMS /
HRRR
where eligible
Stable PRISM → final audit → safe baseline cleanup
Coverage is still being built. Check the inventory—not just the intended era.
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.
1979-01-01 is a partial 11-hour forcing day because NLDAS begins at 13 UTC. It is not a full-day model start. Cleanup is deferred in the active 2003–2020-10-13 campaign. Stable PRISM can change under a major source dataset release; preserve version provenance. HRRR anomaly refinement is not validated/enabled as a retrospective default.

## Slide 16
PRODUCT GUIDE
One daily file; two clocks to understand
Storage dates and physical accumulation intervals are intentionally separate.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
16
Files on disk
Day D: 00 … 23 UTC
Day D+1: 00 …
24-hour NWM
run
Reads D 01 … D+1 00
PRISM rain day
12–12 UTC window → recombine to calendar files
For a full UTC-day simulation, also supply hour 00 from the next file.
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.

## Slide 17
PRODUCT GUIDE
Quality safeguards users should know
A complete file is necessary—but not evidence of perfect accuracy.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
17
CNRFC precipitation
Since July 2020: use trusted 6-hour totals,
not striped hourly timing.
Coverage envelope
Fill required active cells; control offshore
extrapolation.
Physics + publication
Check coupled fields, timestamps, source
provenance and file integrity.
Known limits
No universal “best source”; independent
validation remains future work.
Fine spacing + stable status + model-read success ≠ proven accuracy.
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.

## Slide 18
PRODUCT GUIDE
Find, inspect, then use
Consumers need the stream, valid-hour coverage and publication provenance.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
18
forcing/outputs/conus/{nrt,retro}/YYYY/MM/
YYYYMMDD.LDASIN_DOMAIN1
Choose stream
NRT for operational
replay
Retro for stable history
Check status
python bin/
report_forcing_status.py
Check interval
24 records per day
Next-day 00 for NWM
Save source/version metadata with your experiment. NRT files can change.
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.
Run from repository root in the hydro-ops environment: python bin/report_forcing_status.py. JSON: python bin/report_forcing_status.py --format json --output forcing/status/forcing-status.json. Status scans filenames/metadata, not a full scientific audit. Daily files deliberately have no .nc suffix. Baseline is an intermediate, not an alternative public stream.

## Slide 19
PRODUCT GUIDE
What is ready—and what is not yet promised
User expectations as of 19 September 2026
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
19
Implemented + tested
Required GFS northern fallback
NLDAS arrival / PRISM revisions
Separate NRT and Retro products
Failure-safe publication
Still gated
Live cron coordination
Consistent sub-hour delivery
Partial-current-day publication
Independent accuracy validation
Use the latest inventory for availability; use provenance for reproducibility.
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.

## Slide 20
REFERENCE / OPTIONAL APPENDIX
Source guide & further reading
Official provider details and project methods are linked in slide notes.
HYDRO OPS / FORCING PRODUCTS / DESIGN SNAPSHOT: 19 SEP 2026
20
NOAA / NASA
MRMS • Stage-IV • HRRR • GFS
NLDAS-2 forcing documentation
Oregon State PRISM
Daily update calendar
Grid definitions and revisions
Project documentation
Forcing production workflow
NRT GFS operations + time conventions
Acceptance evidence
NRT revision and reliability reports
Coverage / quality limitations
Provider specifications describe inputs. Check local availability separately.
Notes: Project references: docs/forcing_production_workflow.md; docs/nrt_gfs_operations.md; docs/nwm_time_conventions.md.
NLDAS: https://ldas.gsfc.nasa.gov/nldas
NLDAS forcing: https://ldas.gsfc.nasa.gov/nldas/v2/forcing
HRRR: https://emc.ncep.noaa.gov/emc/pages/numerical_forecast_systems/hrrr.php
MRMS: https://www.nssl.noaa.gov/projects/mrms/operational/tables.php
MRMS versions: https://inside.nssl.noaa.gov/mrms/past-code-updates/
Stage IV: https://www.emc.ncep.noaa.gov/mmb/research/stage4.FAQ.html
PRISM: https://www.prism.oregonstate.edu/calendar/
PRISM grids: https://prism.oregonstate.edu/data/
GFS: https://www.nco.ncep.noaa.gov/pmb/products/gfs/
Cosgrove: https://doi.org/10.1029/2002JD003118